## Slide 1
AI Non-Mask Detection Application
Material for SE
Jul. 2022
Document Ver.1.01
App: AI Non-Mask Detection

## Slide 2
Contents
Concept
Key Features
Specification
Restrictions
Product Description
Installation & Setup Guide
Camera Installation Standard
Setup Procedure

## Slide 3
Product Description

## Slide 4
1. Concept
Non-mask detection
Automatically detect “Non-mask wearer” and issue an alarm
Key Features
System linkage
Enable linkage with various systems by utilizing a range of alarm output interfaces
Support color masks, designed masks, and various shapes of masks
Support for various types of masks
*Sample image of Non-mask detection.
Model | WV-XAE203W
Product name | AI Non-Mask Detection
Supported Cameras | i-PRO with AI engine 5MP models WV-X1551LN / WV-X2251L / WV-X2551LN i-PRO with AI engine 4K models WV-X1571LN / WV-X2271L / WV-X2571LN

## Slide 5
2. Key Features – System linkage
Linkage with video surveillance system
Enable linkage with other systems by utilizing various alarm output interfaces
Video data /
Additional information on the stream
Video data /
TCP alarm protocol notification
Non-Mask Detection
Video Management Software
WV-ASM300
Network Disk Recorder
NX Series
VIDEO INSIGHT

## Slide 6
2. Key Features – Support for various types of masks
 | Color | Design | Shape
Supported |  |  | 
Not Supported |  |  | 
Example
White
Black
Gray
Light blue
Pink
Beige
Blue
Yellow
Purple
Example
Polka dot
Checkered
Tile pattern
Fashion masks
Example
Flat
Three dimensional
Pleated
N95
- Illustration of nose and mouth
- Transparent
- Full face cover
Ex. gas mask

## Slide 7
3. Specification
Detection Standard *1
Minimum detection size (Face width) | 5MP models | 60 pix
 | 4K models | 80 pix
Max. number of simultaneous detection | 8 people | 
Condition for alarm occurrence | Detect a non-mask wearer for two seconds or longer | 
Color/ Black and white | Color: supported / Black and white: NOT supported | 
Installation environment | Indoor / 80 lux or more | 
Angle of face | Right and left: within 45°, Up and down: within 30° | 
Sample face images recognized as mask wearers
Facing front with a mask on
Looking sideways
(right and left: 45°, up and down: 30°)
Wearing glasses and a mask
Wearing a hat and a mask (eyebrows not covered)
(*1) Note that those are theoretical values and
are not guaranteed.

## Slide 8
4. Restrictions
This application does not work when “90°” or “270°” is selected for [Image rotation].
This application may not detect non-mask wearers when:
- wearing a mask under the chin and the nose and mouth are not covered
- covering the mouth with a hand and so on
- outline of the mouth is covered with beard
This application may detect the followings as non-mask wearers:
- dolls, human in a poster, and so on
Software specification related
Other
Performance related
As for the restrictions when installing multiple extension software applications on a camera, refer to the support information “Compatibility list for extension software <C0103>” at the link below.
https://i-pro.com/global/en/surveillance/training-support/support/technical-information

## Slide 9
Installation & Setup Guide

## Slide 10
Recommended cameras
Product name | i-PRO with AI engine 5MP models
Model | WV-X1551LN / WV-X2251L / WV-X2551LN
Note: i-PRO with AI engine 4K models are not recommended as they do not satisfy the recommended detection size (120 pix or more) and angle of depression at the same time.
*See page 25
Recommended installation environment
1) Face width(a) ≥ 80 pix
2) 5°≤ Angle of depression(θ) ≤ 15°
We recommend the location where subjects walk straight toward the camera, facing front.
Face width(a) can be set to approx. 80 pix when adjusting the width of camera view to 4 people opening the arms.
Adjust the angle of depression from 5°to 15°to capture the front face.
6.4m (21ft)
a
θ
θ
1. Camera Installation Standard – Install on the ceiling

## Slide 11
1. Camera Installation Standard – Install on the ceiling
7m
(23ft)
Face width at start point (S) |  |  |  |  | 121pix |  | 95pix |  | 78pix |  | 66pix |  | 57pix
Angle of depression at end point (E) |  |  |  |  | 17.3° |  | 12.2° |  | 9.4° |  | 7.6° |  | 6.4°
5m
(16.4ft)
9m
(29.5ft)
Face detection start point (S)
Distance from face detection start point (S)
3.0m
(9.8ft)
11m
(36.1ft)
13m
(42.7ft)
1.6m (5.3ft)
15m
(49.2ft)
Face detection area
Required face detection area is approx. 2.5m (8.2ft) or more.
= Walking speed (approx. 1.2m (3.9ft)/s) x Travel time (2s)
Recommended area for camera installation
End point (E)
Reference: Distance between camera and subject
Product name | i-PRO with AI engine 5MP model
Model | WV-X1551LN / WV-X2251L / WV-X2551LN
Mounting height | 3.0m (9.8ft)
Zoom ratio | x3.1 *Maximum optical zoom ratio
Conditions

## Slide 12
2. Setup Procedure – Flowchart
The following flowchart describes required settings for the linkage with video surveillance system.
Preparation
Camera settings
Recorder settings
Install the extension software “WV-XAE203W” on the camera.
*For details, refer to the instruction manuals of WV-XAE203W
https://i-pro.com/global/en/surveillance/training-support/documentation-database-list
Configure schedule and TCP alarm protocol notification.
Configure extension software alarm, camera site alarm, schedule, recording setup, and TCP alarm protocol notification.
ASM300 settings
Configure extension software alarm and TCP alarm protocol reception.

## Slide 13
2. Setup Procedure – Camera settings
Configure schedule and TCP alarm protocol notification.
*As for TCP alarm protocol notification setting, refer to the “Appendix” chapter described later.
Schedule setting
Operating day of week
Select the day of week to activate AI Non-Mask Detection for “Time table 1” and “Time table 2”.
AI Non-Mask Detection does not operate on the day of week with “Off” selected.
Time table
Set the time to activate AI Non-Mask Detection, and operation content(On/Off). Up to 6 operating times can be set respectively for [Time table 1] and [Time table 2].
Extension software
Select “AI Non-Mask Detection”.
*Default setting = 24-hour operation

## Slide 14
2. Setup Procedure – Recorder settings
Configure extension software alarm, camera site alarm, schedule, recording setup, and TCP alarm protocol notification. *As for the settings other than extension software alarm, refer to the “Appendix” chapter described later.
Extension software alarm setting
Extension software alarm
Go to [REC & event]-> [Advanced setup] tab -> [Extension software alarm], and click “Setup” to open the [Extension software alarm] setup screen.
Name
Enter the name of alarm.
Ex. “AI Non-Mask Detection”
Message ID
Enter “69” as an ID for AI Non-Mask Detection alarm.
No.
No.1-4: reserved for AI-VMD
No.5-8: available
Set AI Non-Mask Detection alarm in an available line from No.5 to 8.

## Slide 15
Intruder
Loitering
Direction
Cross Line
User-defined 1
User-defined 2
User-defined 3
User-defined 4
2. Setup Procedure – ASM300 settings
Configure extension software alarm and TCP alarm protocol reception.
*As for TCP alarm protocol notification setting, refer to the “Appendix” chapter described later.
Extension software alarm setting
Name
Enter the name of alarm.
Ex. “AI Non-Mask Detection”
Message ID
Enter “69” as an ID for AI Non-Mask Detection alarm.
No.
No.1-4: reserved for AI-VMD
No.5-8: available
Set AI Non-Mask Detection alarm in an available line from No.5 to 8.

## Slide 16
Appendix

## Slide 17
Alarm Linkage Setting

## Slide 18
Setup Flow
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
(1)
(2)
(3)
To perform event recording on the recorder or pop-up alarm notification on WV-ASM300 triggered by AI-VMD, configure the alarm linkage in the following order: 1. Camera, 2. NX series recorder and 3. WV-ASM300.
System Configuration (Ex.)
Alarm notification
192.168.0.250
192.168.0.200
192.168.0.21
WV-XAE203W
.ext
WV-X1551LN
Camera
Recorder
Extension
software
(1)
(2)
(3)
NX series
ASM300
Monitoring software

## Slide 19
Camera Settings – TCP alarm protocol notification
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setup > Alarm > Notification > TCP alarm protocol notification
192.168.0.250
Set [TCP alarm protocol] to “On”
Tick “Alarm” and input IP address of NVR
Set [Additional alarm data] to “On”

## Slide 20
Recorder Settings – Camera site alarm
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setup > REC & event > Event setup > Camera site alarm
Set the [Mode] option to “Recording & alarm action”

## Slide 21
Recorder Settings – Schedule
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setup > REC & event > Recording setup > Schedule
Set [TCP alarm protocol] to “On”
Set [Event recording] to “On”

## Slide 22
Recorder Settings – Recording setup
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setup > REC & event > Recording setup
Set proper schedule to target cameras

## Slide 23
Recorder Settings – TCP alarm protocol
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setup > Network > TCP alarm protocol
Type ASM300 IP Address here.
This is Alarm destination.

## Slide 24
ASM300 Settings – TCP alarm protocol reception
Camera Settings
ASM300 Settings
Recorder Settings
Site alarm
Schedule
Recording
TCP alarm
Alarm reception
TCP alarm
Setting > Communication > TCP alarm protocol reception
Set [Alarm notification (TCP alarm protocol notification)} to “ON”

## Slide 25
Distance between Camera and Subject [4K models]

## Slide 26
Distance between Camera and Subject [4K models]
Face width at start point (S) |  |  |  |  | 108pix |  | 85pix |  | 69pix |  | 59pix |  | 51pix
Angle of depression at end point (E) |  |  |  |  | 17.3° |  | 12.2° |  | 9.4° |  | 7.6° |  | 6.4°
Product name | i-PRO with AI engine 4K model
Model | WV-X1571LN / WV-X2271L / WV-X2571LN
Mounting height | 3.0m (9.8ft)
Zoom ratio | x2 *Maximum optical zoom ratio
Conditions
Note: i-PRO with AI engine 4K models are not recommended as they do not satisfy the recommended detection size (120 pix or more) and tilt angle at the same time.
Face detection start point (S)
Face detection area
End point (E)
Distance from face detection start point (S)
7m
(23ft)
5m
(16.4ft)
9m
(29.5ft)
11m
(36.1ft)
13m
(42.7ft)
15m
(49.2ft)
3.0m
(9.8ft)
1.6m (5.3ft)
Required face detection area is approx. 2.5m (8.2ft) or more.
= Walking speed (approx. 1.2m (3.9ft)/s) x Travel time (2s)

## Slide 27
Evaluation Results

## Slide 28
Evaluation Results from Each Environment
Location (i-PRO office) | Time of day | Illuminance | Number of cases |  | True positive | False positive | False negative
 |  |  | Mask wearer | Non-mask wearer |  |  | 
Bldg. E, 1st floor | 10:00am - 9:00pm | 100 lux - 150 lux | 300 | 90 | 91.1% (81/90) | 0.3% (1/300) | 8.9% (9/90)
Bldg. E, 6th floor | 10:00am - 9:00pm | 80 lux - 500 lux | 30 | 16 | 100% (16/16) | 3.3% (1/30) | 0% (0/16)
Room# E312 | 5:00pm - 8:00pm | 80 lux - 240 lux | 33 | - | - | 0% (0/33) | -
Bldg. P, 1st floor | 8:00am - 10:00am | 500 lux - 700 lux | - | 56 | 92.9% (52/56) | - | 7.1% (4/56)
Bldg. P, 3rd floor | 11:00am - 3:00pm | 400 lux - 500 lux | 3 | 6 | 100% (6/6) | 0% (0/3) | 0% (0/6)
Total |  |  | 366 | 168 | 92.2% (155/168) | 0.5% (2/366) | 7.7% (13/168)
True positive rate: Cases correctly detected as non-mask wearers / The number of non-mask wearers
False positive rate: Cases incorrectly detected as non-mask wearers / The number of mask wearers
False negative: Cases of missed alarm / The number of non-mask wearers

## Slide 29
Sample Evaluation Results
 | Building E, 1st floor | Building E, 6th floor
 |  | -
True Positive Example
False Positive Example
Wearing a beige mask under backlight condition
False Negative Example
Looking sideways
Wearing a beige mask under backlight condition
People overlapped

## Slide 30
Version History

## Slide 31
Version History
No | Update contents | Page No. | Version | Update
1 | 1st Version | - | 1.00 | 17.Dec.2020
2 | Support company name change | - | 1.01 | 14. Jul. 2022
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  |